## Slide 1
Computed Radiography
2007 - Feb

## Slide 2
The Computed Radiography System Computed radiography is performed by a system
consisting of the following functional components
• A digital image receptor (The Imaging Plate) • A digital image processing unit • An image management system • Image and data storage devices • Interface to a patient information system • A communications network • A display device with viewer operated controls

## Slide 3
Computed Radiography (CR) is a process of capturing
Radiographic data from a conventional X-ray machine
and processing the data digitally to produce high quality
Radiographic image.
For exposure , an imaging plate(IP) is placed in a cassete instad of a piece of film.The IP captures and stores the X-ray.
The image is developed in a CR reader instead of a film processor. The CR reader extracts the information stored in the plate and produces a digital image.

## Slide 5
The imaging plate is coated with photostimulable phosphor, also called storage phosphor.
The phosphor material is generally a kind of Bariumfluorohalide.
The imaging plate contains not only the phosphor layer, but also a protective coat, a conductive layer, support and laminate layers.

## Slide 6
When exposed to x-rays, electrons in the phosphor plate are excited into a higher energy state, forming a latent image.
An image reader scans the phosphor plate with a laser spot. When the trapped electrons absorb the laser energy, they emit light as they return to their ground state.
This light is collected by a light guide and transmitted to a photomultiplier tube, which produces an analog electrical signal that is amplified, converted to a digital signal, and digitally stored. The plate can be reused after it is exposed to an erasing light that removes residual radiation.

## Slide 7
Advantages
Computed radiography compared with conventional film/screen combinations include improved contrast resolution and post processing capabilities.
Disadvantages
Imaging plates(IP’s) are quite expensive and can be easily damaged. Result in damage to the IP, for image artifacts.

## Slide 8
Thank You
2007 - Feb